## Slide 1: Lecture 11: RISC-V Processor Datapath

## Slide 2: Recap: Complete RV32I ISA
Not in CS61C

## Slide 3: State Required by RV32I ISA
Each instruction reads and updates this state during execution:
Registers (x0..x31)
  Register file (or regfile) Reg holds 32 registers x 32 bits/register: Reg[0].. Reg[31]
  First register read specified by rs1 field in instruction
  Second register read specified by rs2 field in instruction
  Write register (destination) specified by rd field in instruction
  x0 is always 0 (writes to Reg[0]are ignored)
Program Counter (PC)
  Holds address of current instruction
Memory (MEM)
  Holds both instructions & data, in one 32-bit byte-addressed memory space
  We’ll use separate memories for instructions (IMEM) and data (DMEM)
    Later we’ll replace these with instruction and data caches
  Instructions are read (fetched) from instruction memory (assume IMEM read-only)
  Load/store instructions access data memory

## Slide 4: One-Instruction-Per-Cycle RISC-V Machine
On every tick of the clock, the computer executes one instruction
Current state outputs drive the inputs to the combinational logic, whose outputs settles at the values of the state before the next clock edge
At the rising clock edge, all the state elements are updated with the combinational logic outputs, and execution moves to the next clock cycle
Reg[]
pc
IMEM
DMEM
Combinational Logic
clock

## Slide 5: Basic Phases of Instruction Execution
IMEM
+4
rs2
rs1
rd
Reg[]
ALU
DMEM
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux
Clock
time

## Slide 6: Implementing the add instruction
add rd, rs1, rs2
Instruction makes two changes to machine’s state:
  Reg[rd] = Reg[rs1] + Reg[rs2]
  PC = PC + 4

## Slide 7: Datapath for add
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
RegWriteEnable
(RegWEn)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
+
alu

## Slide 8: Timing Diagram for add
1000
1004
PC
1004
1008
PC+4
add x1,x2,x3
add x6,x7,x9
inst[31:0]
Clock
time
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
+
RegWEn
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
clock
alu
Reg[2]
Reg[7]
Reg[rs1]
Reg[2]+Reg[3]
alu
Reg[7]+Reg[9]
Reg[3]
Reg[9]
Reg[rs2]
???
Reg[1]
Reg[2]+Reg[3]

## Slide 9: Implementing the sub instruction
sub rd, rs1, rs2
Almost the same as add, except now have to subtract operands instead of adding them
inst[30] selects between add and subtract

## Slide 10: Datapath for add/sub
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
RegWEn
(1=write, 0=no write)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel
(Add=0/Sub=1)

## Slide 11: Implementing other R-Format instructions
All implemented by decoding funct3 and funct7 fields and selecting appropriate ALU function

## Slide 12: Implementing the addi instruction
RISC-V Assembly Instruction:
  addi x15,x1,-50
10/1/2018
111111001110
00001
000
01111
0010011
OP-Imm
rd=15
ADD
imm=-50
rs1=1

## Slide 13: Datapath for add/sub
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
RegWEn
(1=write, 0=no write)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel
(Add=0/Sub=1)

## Slide 14: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1

## Slide 15: I-Format immediates
inst[31:0]
------inst[31]-(sign-extension)-------
inst[30:20]
imm[31:0]
Imm.
Gen
inst[31:20]
imm[31:0]
ImmSel=I
High 12 bits of instruction (inst[31:20]) copied to low 12 bits of immediate (imm[11:0])
Immediate is sign-extended by copying value of inst[31] to fill the upper 20 bits of the immediate value (imm[31:12])

## Slide 16: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel

## Slide 17: TSMC Announces 3nm CMOS Fab
Latest Apple iPhone 8, iPhone X use TSMC’s 10nm process technology.
3nm technology should allow 10x more stuff on the same sized chip (10/3)2
The new manufacturing plant will occupy nearly 200 acres and cost around $15B, open in around 5 years (~2022).
Currently, fabs use 193nm light to expose masks
For 3nm, some layers will use Extreme Ultra-Violet (13.5nm)

## Slide 18: Break!

## Slide 19: Implementing Load Word instruction
RISC-V Assembly Instruction:
  lw x14, 8(x2)
10/1/2018
000000001000
00010
010
01110
0000011
LOAD
rd=14
LW
imm=+8
rs1=2

## Slide 20: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1

## Slide 21: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BSel
ALUSel
MemRW
WBSel
wb

## Slide 22: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=0
wb

## Slide 23: All RV32 Load Instructions
Supporting the narrower loads requires additional circuits to extract the correct byte/halfword from the value loaded from memory, and sign- or zero-extend the result to 32 bits before writing back to register file.
funct3 field encodes size and signedness of load data

## Slide 24: Implementing Store Word instruction
RISC-V Assembly Instruction:
  sw x14, 8(x2)
10/1/2018
0000000
01110
00010
010
01000
0100011
STORE
offset[4:0]
=8
SW
offset[11:5]
=0
rs2=14
rs1=2
combined 12-bit offset = 8
0000000
01000

## Slide 25: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BSel
ALUSel
MemRW
WBSel
wb

## Slide 26: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
Bsel
ALUSel
MemRW
WBSel=
wb

## Slide 27: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=S
RegWEn=0
Bsel=1
ALUSel=Add
MemRW=Write
WBSel=*
wb
*= “Don’t Care”

## Slide 28: I-Format immediates
inst[31:0]
------inst[31]-(sign-extension)-------
inst[30:20]
imm[31:0]
Imm.
Gen
inst[31:20]
imm[31:0]
ImmSel=I
High 12 bits of instruction (inst[31:20]) copied to low 12 bits of immediate (imm[11:0])
Immediate is sign-extended by copying value of inst[31] to fill the upper 20 bits of the immediate value (imm[31:12])

## Slide 29: I & S Immediate Generator
imm[11:5]
rs2
rs1
funct3
imm[4:0]
S-opcode
imm[11:0]
rs1
funct3
rd
I-opcode
inst[31](sign-extension)
inst[30:25]
imm[31:0]
inst[31:0]
inst[24:20]
S
I
inst[31](sign-extension)
inst[30:25]
inst[11:7]
0
6
7
11
12
14
15
19
20
24
25
31
0
4
5
10
11
31
1
6
5
5
S
I
Just need a 5-bit mux to select between two positions where low five bits of immediate can reside in instruction
Other bits in immediate are wired to fixed positions in instruction

## Slide 30: Implementing Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)

## Slide 31: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
Bsel
ALUSel
MemRW
WBSel=
wb

## Slide 32: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 33: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=0
BrUn
BrEq
BrLT
ASel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=*
PCSel=taken/not-taken
wb

## Slide 34: Branch Comparator
BrEq = 1, if A=B
BrLT = 1, if A < B
BrUn =1 selects unsigned comparison for BrLT, 0=signed
BGE branch: A >= B, if !(A<B)
Branch Comp.
A
B
BrUn
BrEq
BrLT

## Slide 35: Administrivia (1/2)
Midterm 1 has been graded!
Regrade Requests will open tonight
  Due next Tuesday (in one week)
  Piazza will explain the instructions

## Slide 36: Administrivia (2/2)
Project 1 has been released
  Part 1 is due next Monday
  Project Party in Cory 293 on Wednesday 7-9pm (possibly later if needed)
Homework 2 is due this Friday at 11:59pm
  Will help to do this before the project!
No Guerrilla Session this week—will start up again next Tuesday

## Slide 37: Break!

## Slide 38: Multiply Branch Immediates by Shift?
12-bit immediate encodes PC-relative offset of -4096 to +4094 bytes in multiples of 2 bytes
Standard approach: treat immediate as in range -2048..+2047, then shift left by 1 bit to multiply by 2 for branches
s
rs2
rs1
funct3
imm[4:0]
B-opcode
imm[10:5]
s
imm[10:5]
imm[4:0]
s
imm[10:5]
imm[4:0]
0
sign-extension
sign-extension
S-Immediate
B-Immediate (shift left by 1)
Each instruction immediate bit can appear in one of two places in output immediate value – so need one 2-way mux per bit

## Slide 39: RISC-V Branch Immediates
12-bit immediate encodes PC-relative offset of -4096 to +4094 bytes in multiples of 2 bytes
RISC-V approach: keep 11 immediate bits in fixed position in output value, and rotate LSB of S-format to be bit 12 of B-format
sign=imm[11]
imm[10:5]
imm[4:0]
sign=imm[12]
imm[10:5]
imm[4:1]
0
S-Immediate
B-Immediate (shift left by 1)
Only one bit changes position between S and B, so only need a single-bit 2-way mux
imm[11]

## Slide 40: RISC-V Immediate Encoding
Instruction Encodings, inst[31:0]
32-bit immediates produced, imm[31:0]
Only bit 7 of instruction changes role in immediate between S and B
Upper bits sign-extended from inst[31] always

## Slide 41: Implementing JALR Instruction (I-Format)
JALR rd, rs, immediate
  Writes PC+4 to Reg[rd] (return address)
  Sets PC = Reg[rs1] + immediate
  Uses same immediates as arithmetic and loads
    no multiplication by 2 bytes

## Slide 42: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 43: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 44: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 45: Implementing jal Instruction
JAL saves PC+4 in Reg[rd] (the return address)
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions
Immediate encoding optimized similarly to branch instruction to reduce hardware cost

## Slide 46: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 47: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 48: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 49: And in Conclusion, …
Universal datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF, ID, EX, MEM, WB
  Not all instructions are active in all phases
Controller specifies how to execute instructions
  what new instructions can be added with just most control?